TightGate-Pro

Dediziertes Remote-Controlled Browser System
zum Schutz vor Gefahren aus dem Internet

Automatisch generierter Auszug aus dem Administrationshandbuch

Datum: 11.04.2019

Herausgeber:
m-privacy GmbH
Technische Redaktion
Werner-Voß-Damm 62
12101 Berlin

Fon: +49 30 243423-34

support@m-privacy.de
www.help.m-privacy.de

Allgemeine Hinweise zu diesem Handbuch
Alle Materialien und Ausführungen wurden mit Sorgfalt erarbeitet und zusammengestellt. Den­noch sind Fehler nicht auszuschließen. Die m-privacy GmbH übernimmt keine Haftung für Schäden, die aus Unrichtigkeit einzelner Angaben entstehen.
Im Sinne einer raschen Orientierung und zur Vermeidung von Sicherheitsrisiken werden besonders wichtige Aspekte durch wiederkehrende Stichworte gekennzeichnet. Diese sind:
Hinweis
Unter diesem Stichwort werden nützliche Details zur rationellen Verwendung von TightGate-Pro er­läutert.
Achtung
Unter diesem Stichwort erfolgen Hinweise zur Problemvermeidung bzw. zur Vorbeugung von Betriebs­störungen bei TightGate-Pro.
Warnung
Unter diesem Stichwort erfolgen Hinweise auf mögliche Fehler bei der Konfiguration und Verwendung von TightGate-Pro, die weitreichende Sicherheitsrisiken bergen oder zu schwerwiegenden Betriebs­störungen führen können.

# Network specifications and connection paths
The following overview describes all ports and protocols that are required for the operation of TightGate-Pro in the network. An internal firewall (packet filter or layer 3 switch) must be provided by the operator.

## Firewall settings
TightGate-Pro is designed for use in a demilitarised zone (DMZ). It must be ensured that workstations in the internal network only connect to TightGate-Pro via the designated ports. In addition, suitable firewall or packet filter rules must be used to prevent internal systems from reaching the Internet directly by bypassing TightGate-Pro.
Connection paths that are not required for regular operation must be marked as optional labelled as optional. They should be deactivated if the corresponding functions are not used.
### Outgoing connections
For UDP connections, the associated response packets must also be authorised.
Sender	Destination	Protocol	Port(s)	Remark	Optional
TightGate-Pro	Internet	TCP	80, 443 or proxy port	HTTP(S) access to the Internet. If a proxy is connected upstream, its port must be released.
TightGate-Pro	m-privacy Update server TCP 22 or 443 or proxy SSH access to the update servers of .			m-privacy GmbH See: Configuration settings for the update.
TightGate-Pro	Internet	UDP	80, 443, 1024:65535	Use of WebRTC services (e.g. Webex, Zoom). Depending on the provider, further authorisations may be required. See: List of supported web meeting platforms.	X
TightGate-Pro	specific	UDP	123	NTP requests	X
TightGate-Pro	specific	TCP + UDP	53	DNS queries	X
TightGate-Pro	specific	TCP	25	For e-mail use: POP3: 110 / POP3-SSL: 995 / IMAP4: 143 / IMAP4-SSL: 993	X
TightGate-Pro	specific	TCP + UDP	88	Kerberos communication	X
TightGate-Pro	specific	TCP	389,636 3268,3269	LDAP/LDAPS and queries of the global catalogue	X
TightGate-Pro	specific	TCP	22, specific	Direct access to SSH or HTTP server	X
TightGate-Pro	specific	TCP + UDP	514,2514,3514	Configurable ports for Syslog/RELP/RELP-TLS. See: Playing out syslog messages to central syslog servers.	X
TightGate-Pro	specific	TCP UDP	3389,1494,80,443 1604	Communication with RDP or Citrix servers (incoming and outgoing)	X

### Incoming connections (LAN)
Originator	Destination	Protocol	Port(s)	Remark	Optional
Clients (workstation PC)	TightGate-Pro	TCP	5900	TLS-encrypted connection of the TightGate-Viewers to TightGate-Pro.
Clients (workstation PC)	TightGate-Pro	TCP	22	SFTP access for the file transfer.	X
Administration network	TightGate-Pro	TCP	222 2222 22222	SSH access for administration. If no admin port is selected, access is via port 22.	X

### Incoming connections (DMZ/Internet)
Sender	Destination	Protocol	Port(s)	Remark	Optional
Internal DNS service	TightGate-Pro Cluster system	UDP TCP	53	Only required when using a cluster. TCP-53 is required if responses exceed the maximum UDP packet size.	X
SNMP monitoring	TightGate-Pro	UDP	161	SNMP requests	X
NRPE monitoring	TightGate-Pro	TCP	5666	Access from ZenTiV or other NRPE-based monitoring systems	X